## Slide 1: Components
HP and IP
  Rotor
  Diaphragm
  Blades/Nozzles
  Casing
LP
  Rotor
  Diaphragm
  Blades/nozzles

## Slide 2: List of Potential Materials HP, High T, Static and Dynamic
Inconel 617
Inconel 625
Inconel 718
Inconel 740
Nimonic 105
Nimonic 115
Nimonic 263
Haynes 230
Haynes 282
U700
U710
U720
Waspaloy
ODS-FeCrAl

## Slide 3: Phase 1 – Disqualifying Factors HP Components–Rotor, diaphragm, casing
Weldability
(Ti+Al )< 2.5
Yes - Inconel 617, Inconel 625, Inconel 718, Haynes 230, Inconel 740, Nimonic 263
No U720, Waspalloy, Nimonic 105, Nimonic 115, Haynes 282
Larson-Miller
Parameter >25k
Yes - Inconel 617, Inconel 740, Nimonic 263
No - Inconel 625, Inconel 718, Haynes 230
Machinability
Yes - Inconel 617, Inconel 740, Nimonic 263

## Slide 4: Phase 2 - Performance Ranking HP/IP Rotor, Diaphragm and Casing
Material | Yield Strength (Mpa) | Cost ($/lb) | $/sy (x100) | Oxidation Rank
Inconel 617 | 283 | 10.70 | 3.78 | 8
Inconel 740 | 608 | 10.70 | 1.76 | 10
Nimonic 263 | 630 | 11.39 | 1.81 | 6

## Slide 5: Phase 1 – Disqualifying Factors HP Components – Blades
Weldability
N/A
N/A
Larson-Miller
Parameter >25k
Yes - Inconel 617, Inconel 740, Nimonic 263, Nimonic 105, Nimonic 115, U720, Waspaloy, Haynes 282
No - Inconel 625, Inconel 718, Haynes 230
Machinability
Yes - Inconel 617, Inconel 740, Nimonic 263,Nimonic 105, Nimonic 115, Waspaloy, Haynes 282
No – U720

## Slide 6: Phase 2 - Performance Ranking HP Blades
Material | Yield Strength (Mpa) | Cost ($/lb) | $/sy (x100) | Oxidation Rank
Inconel 617 | 283 | 10.70 | 3.78 | 8
Inconel 740 | 608 | 10.70 | 1.76 | 10
Nimonic 263 | 630 | 11.39 | 1.81 | 6
Nimonic 105 | 690 | 11.36 | 1.65 | 9
Nimonic 115 | 690 | 11.36 | 1.65 | 9
Waspaloy | 650 | 10.30 | 1.58 | 5
Haynes 282 | 614 | 10.35 | 1.69 | 6

## Slide 7: List of Potential Materials LP Components
304
316Ti
A286
253MA

## Slide 8: Phase 1 – Disqualifying Factors LP Components
Weldability
(Ti+Al )< 2.5
Yes – 304, 316Ti, 253MA, A286
Larson-Miller
Parameter
N/A
Machinability
Yes – 304, 316Ti, 253MA, A286

## Slide 9: Phase 2 - Performance Ranking LP Rotor, Diaphragm and Blades
Material | Yield Strength (Mpa) | Cost ($/lb) | $/sy (x100)
316Ti Stainless | 160 | 2.95 | 1.84
304 Stainless | 200 | 2.21 | 1.11
253MA | 202 | 2.64 | 1.31
A286 | 510 | 3.95 | 0.77